## Slide 1: ENGI 301 Colorful Melodies - Proposal
10/19/2019
Jorge F. Tito-Arce

## Slide 2: Background Information
Using color sensors, buzzers with musical ranges, and an embedded computing system, the curious tinkerer can convert a string of colors to sounds.
Previous project by Yuri Suzuki: Music from Art
  Color Chaser 2010: Follows a black line and reads the colors painted on that line
  People can add whatever color they want, thus contribute directly to the music being produced.
  https://vimeo.com/72853276
Improvements with my design:
  Stationary
  Use circle properties to create a melodic sound: like a CD, but can be interacted with by coloring specific parts

## Slide 3: Design
1
3
4
2
9
6
7
8
5

## Slide 4: Bill of Materials
Number on Drawing | Name
1 | Color Wheel
2 | Top and Bottom Plates
3 | Color Sensor
4 | D.C. Motor
5 | Beagle Bone
6 | Pillars
7 | USB Audio Adapter, Speaker
8 | Hex Display for tempo
9 | Variable Resistor

## Slide 5: Design Intent
To allow users to interact with the music they want to hear
  Can color in pre-made disks or even make their own disks
  Can slow down the tempo by having a variable resistance to the motor driving the color wheel
To show the connection between visual and audio stimuli
  Robot with synesthesia
  Appreciation of the arts in a technical world

## Slide 6: System Block Diagram
Color Sensor
DC Motor
Variable Resistor
Pocket
Beagle
I2C1
SYS
USB 1
Speaker
Hex Display for Tempo
I2C2
AIN

## Slide 7: Power Block Diagram
Color Sensor
DC Motor
Variable Resistor
Pocket
Beagle
I2C1
3.3V
Out
USB1
USB Audio Adapter
Hex Display for Tempo
I2C2
110 mA
3.3V
330 µA max
PWM1
3.3 V
2 mA max
3.3 V
USB0
Power In

## Slide 8: Components / Budget
Component | Need to Buy | Cost
AdaFruit Color Sensor | Yes | $7.95
DC Motor | Yes | $1.95
Plugable USB Audio Adapter | Yes | $14.99
PocketBeagle | No | 
Hex Display | No | 
Variable Resistor | Yes | $4.59
Wood | Yes/No | ~$20.00
Speaker | No | 
Total: 49.48